## Slide 1: Naval Sea Systems Command (NAVSEA) Nondestructive Testing (NDT)
Jason Hence
NAVSEA NDT & Welding Programs Manager
DoD Joint Technology Exchange Group (JTEG)
Nondestructive Inspection (NDI) Forum
Distribution Statement A: Approved for Public Release; Distribution is Unlimited

## Slide 2: NAVSEA NDT
NAVSEA NDT Working Group
Phased Array Ultrasonic Testing (PAUT) / Time of Flight Diffraction (ToFD)
Computed Radiography (CR)
Terahertz Imaging

## Slide 3: NDT Working Group

## Slide 4: NDT Working Group
2017 NDT WG Meeting – NSWC Port Hueneme Division

## Slide 5: NDT Working Group
History
  Various forms of the NDT Working Group date back to the mid-1980’s
  Current version began in 2001

## Slide 6: NDT Working Group
Vision
  To be the instrument for making or recommending improvements to NAVSEA-specified NDT processes.

## Slide 7: NDT Working Group
Purpose:
  Address and resolve, or recommend resolution to NDT issues associated with building, maintaining, and operating Naval ships.
  Share ideas, information, successes, best practices, and failures.
  Make improvements through effective integration of all stakeholders.
  Receive guidance, approval, support, and/or limitations from NAVSEA 04X6.
  Determine applicable action items.
  Address improvement of NDT processes from an industry-wide perspective.

## Slide 8: NDT Working Group
Membership
  Chairperson: NDT Program Manager
  NAVSEA NDT Technical Representative: NDT & E Technical Warrant Holder
  Host: Rotational among stakeholders
  Stakeholders:
    NAVSEA
    Naval Shipyards
    Shipbuilders
    Regional Maintenance Centers
    Supervisors of Shipbuilding (SUPSHIP)
    Contractors who perform NAVSEA-specified NDT
    Fleet activities
    Naval Warfare Centers
    Defense Contract Management Agency (DCMA)

## Slide 9: NDT Working Group
Meeting Format (3 days)
  Presentations (Kept to a minimum)
    State of NAVSEA NDT (NAVSEA NDT TWH)
    Working Group Action Item Updates (NAVSEA NDT Program Manager)
    Significant NDT Audit Findings (NAVSEA NDT Program Manager)
    Emerging NDT Technology
  Breakout Sessions
  Finalize Action Items

## Slide 10: NDT Working Group
Accomplishments
  Revised NAVSEA NDT Standards
  Phased Array Ultrasonic Testing (PAUT) requirements
  Computed Radiography (CR) requirements

## Slide 11: Phased Array Ultrasonic Testing (PAUT) / Time of Flight Diffraction (ToFD)

## Slide 12: Phased Array UT / ToFD
What is it?
  PAUT
    Multiple elements (up to 256) and electronic time delays to create beams that can be steered, swept, scanned, and focused electronically
    Full data storage with encoding (recording)
      Reference for future inspections on the same site
    Multiple angle concurrent inspections
  Conventional UT
    Manual scanning using single element, fixed angle transducer
    No permanent record of raw data
    Characterization and Sizing (UTCS) requires multiple set-ups, several angles (transducers), significant time

## Slide 13: Phased Array UT / ToFD

## Slide 14: Phased Array UT / ToFD
Conventional Shear Wave

## Slide 15: Phased Array UT / ToFD
ToFD
  Highly sensitive “pitch-catch” technique with capabilities of detecting longitudinal and transverse flaws
  Detects embedded and most surface-connected flaws

## Slide 16: Phased Array UT / ToFD

## Slide 17: Phased Array UT / ToFD
Advantages
  Raw Data Collection
    Data encoded and stored digitally
    Composite images of discontinuities
    Reduced dependence on operator to visually identify flaws while scanning manually
  Repeatability
    Consistent indication location/length measurements
    Increased accuracy for determination of indication growth for baseline and monitoring inspections
  Cost / Schedule Savings
    Less time required for inspections

## Slide 18: Phased Array UT / ToFD
Previous:
  Radiographic Testing on piping welds
  Conventional UT Shear Wave on ship structure

## Slide 19: Phased Array UT / ToFD
Current:
  PAUT / ToFD on piping welds down to 2-½” NPS and limited by minimum wall thickness and configuration:
    Carbon Steel
    Copper-Nickel
  Conventional UT Shear Wave on ship structural applications
    Awaiting approval to use PAUT / ToFD
    Created a draft procedure, provided proof test information to NDT TWH
  Inspection Personnel
    Certified Level III PAUT / ToFD Examiners (PSNS & PHNSY)
    Inspector candidates ready to be examined / certified

## Slide 20: Phased Array UT / ToFD
End State:
  PAUT / ToFD on any piping welds not limited by the material type or configuration
  PAUT / ToFD on all structural applications not limited by configuration (may need to use other NDT (RT or MT every layer) on some configurations)
  PAUT / ToFD for all UT Characterization and Sizing

## Slide 21: Phased Array UT / ToFD
Challenges to Implementation
  High equipment cost
  Additional personnel training / oversight
  Qualification requirements
  Resistance to change
  Personnel turnover / limited resources
  Cybersecurity requirements

## Slide 22: Computed Radiography (CR)

## Slide 23: Computed Radiography (CR)
What is it?
  Radiographic Testing (RT) process that uses digital imaging plates in place of conventional film RT.

## Slide 24: Computed Radiography (CR)
Advantages
  Digital image storage eliminates the need for a physical medium (i.e., film)
  Eliminates film processing equipment, chemicals, etc.
  Radiographic Testing (RT) image sharing over networks

## Slide 25: Computed Radiography (CR)
Current state
  All Radiographic Testing (RT) performed using physical film
  Film is processed (manually or automatically) using chemicals
  Chemical HAZWASTE disposal / Silver recovery
  Film maintained in accordance with fabrication document record retention requirements
  Audits conducted where the film is stored

## Slide 26: Computed Radiography (CR)
End State
  All RT performed using CR
  CR files transferred over Navy networks (e.g., NMCI, UNNPI, etc.)
  Audits of RT records conducted with no travel necessary for the auditor

## Slide 27: Terahertz Imaging

## Slide 28: Terahertz Imaging
Research & Development Phase
Dr. Patric Lockhart (Naval Undersea Warfare Center – Newport)

## Slide 29: Terahertz Imaging
What is it?
  Technology that lets you “see” inside or through many solid objects/coatings to detect defects in a target structure or material lying beneath.
    Debonds, corrosion, voids, water intrusion, mechanical damage, internal interfaces

## Slide 30: Terahertz Imaging

## Slide 31: Terahertz Imaging
Advantage
  Noninvasive detection of defects in certain ship structural applications

## Slide 32: NAVSEA NDT
NAVSEA NDT Working Group
  Annual meeting
PAUT / ToFD
  Partial approval
CR
  Requirements document drafted
Terahertz Imaging
  R&D
  Dr. Patric Lockhart