## Slide 1: USAF Rapid Sustain Office (RSO) Advance Manufacturing Program Office (AMPO)
Advance Manufacturing Program Office I 10.26.2021
Controlled by: RSO
Controlled by: Advance Manufacturing Program Office
CUI Category: N/A
POC: Travis Grohoske
Distribution Statement: A

## Slide 2
DAF Additive Manufacturing Eco-System
Deploy
Standardize
CAPABILITY
Promote DAF adoption of AM:
Prototyping in force
Re-manufacturing aids
Legacy parts & sustainment
New parts and capabilities
Explore
Mature
Evaluate
TECHNOLOGY
DAF
Needs
Materials
Process es
HIGHER EDUCATION
New Advanced Manufacturing requirements
Industry
Notes: -The DAF AM Eco-system includes key leaders from AFRL, AFLCMC, and AFSC for a team approach to developing and adopting AM​
-- It is critical to include partners from academy and industry to gain a competitive advantage ​
-- We focus teams on their strengths with AFRL taking command of lower TRL/MRL projects to mature the technology's​
-- The RSO focus on scaling and developing value in additive manufacturing process with higher readiness levels​
-Proven repeatable process that constantly evaluates the state of DAF Needs, Processes and Materials​

## Slide 3
AM Program Office Execution
Material and Machine Qualification
  Procurement documents
  Material Characterization
  Requirement's definitions
Personnel Certification
  Technician training
  Engineering training
Technical Data
  Periodic maintenance
  Facility guidelines
Maintain Advance Technology and Training Centers (ATTC)
  Dayton, Ohio
  Middle, Georgia

## Slide 4
Capabilities – Printing and Post Process
METAL PRINTERS AND POST PROCESSING
EOS M400-4 (2)
EOS M290 (15)
Delta H Aluminum Furnace (2)
Ipsen Vacuum Furnace (2)
Hexagon Shop Floor CMM (2)
Mitsubishi Wire EDM (3)
Haas CNC Mill (3)
Haas CNC Lathe (2)
Manual Mill (3)
Manual Lathe (2)
Ti-6Al-4V (Titanium)2
17-4PH SS (Stainless Steel)
NA718 (Nickel Alloy)
CoCrMo (Cobalt Chrome)2
AlSi10Mg (Aluminum)
F357 Al (Aluminum)
MATERIALS
POLYMER PRINTERS
Stratasys Fortus F900 (5)
Stratasys Fortus 450mc (3)
Desktop Printers (7)
MATERIALS1
Antero 800NA
ULTEM 9085 Natural2, Certified Grade (CG)
ULTEM 9085 Natural2
ULTEM 9085 Gunship Gray
ULTEM 9085 Black

## Slide 5
Size Limitations
12.8 inches
9.8
9.8
Fused Deposition Modeling (FDM)
Stratasys 450mc F900 equipment
Size: 36 x 24 x 36 inch build volume
POLYMERS
METALS
Direct Metal Laser Melting (DMLM)
EOS M290 equipment
Size: 9.8 x 9.8 x 12.8 inch build volume
24
36
36 inches

## Slide 6
Identified DAF Application Areas
Enhanced Capability
Lead Time Reduction
Affordability
Parts Replacement
Complex Geometries & Integration
Immediate Innovation
Manufacturing Process Aids

## Slide 7
GENERAL APPLICATIONS
Tooling and fixtures
Phenolic replacement (FDM Antero)
Aircraft Polymer panels and covers (FDM Ultem 9085)
Aircraft Polymer ducts (FDM Ultem 9085)
Aircraft Metals Replacement (DMLM)

## Slide 8: C-5 GALAXY
C-5 Upper Forward Service Door Support Original: Aluminum 7075-T6 AM: Titanium Ti-6Al-4V
Aft Ramp Bell Cranks Original: Aluminum 7075-T651 AM: Titanium Ti-6Al-4V
Flight Navigator A/C Diffuser
Original: Painted sheet metal
AM: Ultem 9085
Seal Retention Handle Original: Aluminum A356 AM: Aluminum AlSi10Mg-T6
Ladder Stops
Original: Aluminum 7075-T651
AM: Titanium Ti-6Al-4V
OVER 60 UNIQUE FLYING PART NUMBERS!
Troop Reading Light Mount Original: Phenolic Fiberglass AM: Ultem 9085

## Slide 9: C-130 HERCULES
Utility Hydraulic Panel
Original: Lexan
AM: Ultem 9085
Hydraulic Pump Support
Original: Aluminum 7075
AM: Aluminum AlSi10Mg
Latrine Drip Shield
Original: Plastic
AM: Ultem 9085
Hydraulic Line Bracket Original: Aluminum 6061-T6 AM: Titanium Ti-6Al-4V
Platform Support Fitting
Original: Aluminum A357-T61
AM: Titanium Ti-6Al-4V

## Slide 10: F-16 FIGHTING FALCON
Jet Fuel Starter (JFS) Test Duct
Original: Stainless Steel, 17-4PH
AM: Welded Nickel Alloy 718
Hands-on Throttle And Stick (HOTAS) Paddle Prototype Original: Aluminum 6061-T6
AM: Titanium Ti-6Al-4V
Hydraulic Tubing Support
Original: Nylon 66
AM: Antero 800NA

## Slide 11: ADVANCED M ANUFACTURI NG C-5 AFT RAMP BELL CRANK
ORIGINAL MATERIAL:
Aluminum 7075-T651
AM MATERIAL:
Titanium Ti-6Al-4V
KICKOFF:
APR 2017
FIT CHECK:
NOV 2017
BACKGROUND
These C-5 bell cranks prevent the aft ramp pressure door hinges from over extending. Parts fail due to an extended lifetime of corrosion and wear. Diminishing source of supply results in long lead times for traditional part replacement. DMLM provides an AM solution with a titanium alternative bell crank.
DEVELOPMENT RESULTS
1.5X+ material strength improvement
Planned and executed qualification testing to include dimensional inspection, computerized tomography
(CT) scan, tensile bar test, and component level loading
Proved out failure in shear bolts prior to bell crank failure
Geometry ultimately optimized for light weight using finite element analysis (FEA) simulation
AM process simulation implemented to optimize print process

## Slide 12: ADVANCED M ANUFACTURI NG C-5 INTERIOR PANELS
ORIGINAL MATERIAL:
Kydex/Polymer
AM MATERIAL:
Ultem 9085
KICKOFF:
Various
INSTALL:
Various
BACKGROUND
The C-5 Galaxy has been transporting cargo since 1970. With nearly 50 years of abuse, many of the interior panels and covers have deteriorated beyond repair with no immediate source of supply. FDM has delivered a robust AM solution with Ultem 9085, a polyetherimide polymer which meets stringent flame, smoke, and toxicity (FST) requirements of 14 CFR 25.853 and is approved for aircraft interior applications via Airworthiness Circular AC-18-04.
DEVELOPMENT RESULTS
Tech data packages delivered for 30+ unique P/Ns, with 50+ flying panels
Existing print capabilities available at Travis AFB
Airworthiness Circular to support interior aircraft application approval
3’x2’x3’ part size capability

## Slide 13: ADVANCED M ANUFACTURI NG C-5M HUMP PANEL WEDGE SPACERS AND SUPPORT BLOCKS
ORIGINAL MATERIAL:
Phenolic
AM MATERIAL:
Antero 800NA
WEDGE KICKOFF:
NOV 2018
WEDGE INSTALL:
MAR 2019
BACKGROUND
Wedges and support blocks provide underlying shape of the C-5 upper hump aerodynamic
panel over the wing splice. This panel has exhibited adhesion bond issues with existing
phenolic parts. AM eliminates health hazards with machined phenolic dust. AM Antero 800NA offers a polymer replacement with excellent chemical and thermal performance.
DEVELOPMENT RESULTS
Qualified 84 unique blocks and 12 unique wedges
Integrated components, eliminating over 300 fasteners and 84 sheet aluminum straps per aircraft
Developed bond surface preparation method for existing aircraft sealant
Led qualification testing including ASTM roller peel and fastener pull out combined with chemical and thermal environmental exposure
Lead time and cost savings addressing true air craft readiness issue

## Slide 14: ADVANCED M ANUFACTURI NG C-130 HYDRAULIC PUMP SUPPORT
ORIGINAL MATERIAL:
Aluminum 7075
AM MATERIAL:
Aluminum AlSi10Mg
KICKOFF:
11 NOV 2019
INSTALL:
04 JUN 2020
BACKGROUND
This bracket supports the hydraulic hand pump used for manual operation of the rear cargo ramp when power is down. Existing machined Aluminum 7075 bracket fails frequently (2/month), has zero supply balance and difficulty in local manufacture or procurement.
DEVELOPMENT RESULTS
Laser scan of fractured part for reverse engineered CAD model
FEA and design optimization for ~2X part strength
Designed for AM with minimized post processing and machining
Qualification test plan development and execution with CT scanning and application specific load testing

## Slide 15: ADVANCED M ANUFACTURI NG F-15 ECS LOUVER
ORIGINAL MATERIAL:
Titanium Unalloyed
AM MATERIAL:
Nickel Alloy 718
KICKOFF:
AUG 2019
INSTALL:
SEP 2020
BACKGROUND
The F-15 louver keeps birds and debris from entering the ECS duct system. The original six piece welded assembly experienced frequent failures due to weld cracks between the individual louvers and housing. DMLM delivered a one piece AM design from Nickel Alloy 718 for improved durability and increased temperature performance.
DEVELOPMENT RESULTS
Improved fit to aircraft outer mold line
Increased design robustness with filleted louvers to housing
Increased thermal performance with Nickel Alloy 718
Extended lifecycle for reduced downtime and maintenance hours
Increased aircraft readiness
Weld Crack

## Slide 16: ADVANCED M ANUFACTURI NG F-15, M61 CANNON TURNAROUND GUIDES
ORIGINAL MATERIAL:
Aluminum A356-T6
AM MATERIAL:
Titanium Ti-6Al-4V
KICKOFF:
MAR 2019
PART DELIVERY:
SEP 2019
BACKGROUND
The turnaround guides are part of the ammunition feed system on an M61 Vulcan Cannon. They are a consumable wear item with limited source of supply and long lead times. AM provides a solution with DMLM Titanium Ti-6Al-4V for reduced lead time and increased life cycle.
DEVELOPMENT RESULTS
Prepared four part numbers with minor adjustments for improved printing with DMLM
Produced 36 parts in 3 DMLM builds with minimal post processing
Performed dimensional qualification of all components
Delivered 15 parts to Program Office for live fire qualification testing

## Slide 17: ADVANCED M ANUFACTURI NG HH-60 FLARE DISPENSER
ORIGINAL MATERIAL:
Aluminum 7075
AM MATERIAL:
Titanium Ti-6Al-4V
KICKOFF:
JUN 2019
DELIVERY:
NOV 2020
BACKGROUND
The flare dispenser is mounted on the side of the HH-60 Pave Hawk for the purpose of delivering flares. The existing Aluminum 7075 mounting brackets were exhibiting stress corrosion cracking. DMLM Titanium Ti-6Al-4V provides a robust AM solution for the conversion of the entire Flare Dispenser assembly.
DEVELOPMENT RESULTS
Re-designed mounting features to greatly reduce crack potential
Applied FEA and geometry optimization for increased strength vs weight
Produced 8 AM components for left and right hand assemblies
Developed and executed qualification test plan including strain gaging, impact testing, tensile specimens, and CT evaluation
Successfully fit-checked mounting to HH-60 Pave Hawk

## Slide 18: ADVANCED M ANUFACTURI NG ARNOLD ENGINEERING DEVELOPMENT COMPLEX (AEDC) PRESSURE RAKE TEST RIG
ORIGINAL MATERIAL:
NA
AM MATERIAL:
Stainless Steel 17-4PH
KICKOFF:
AUG 2018
DELIVERED:
MAR 2019
BACKGROUND
A research group at AEDC investigate the printing of a single piece pressure rake test rig for air flow experimentation. Existing pressure rakes are typically multi- piece fabrications with many delicate pitot tubes. The proposed AM rake concept was a single piece rig with four internal rake probes comprising 28 total pitot tubes, each with internal channels routed through the duct to a single outlet port location.
DEVELOPMENT RESULTS
Optimized initial customer design for DMLM to print without support
Successfully printed and cleared powder from 28 channels at .080” diameter and up to 14” long, thus demonstrating feasibility
Leveraged polymer 3D printing for protective packaging
Cross-section and network
of hollow channels
Protective packaging

## Slide 19
Total Parts Delivered
Part Category | Parts Delivered |  |  |  |  |  |  |  | Total Unique Part #s | Total Parts
 | Metal |  |  |  | Polymer |  |  |  |  | 
 | Aerospace |  | Other |  | Aerospace |  | Other |  |  | 
 | Unique Part #s | Total Parts | Unique Part #s | Total Parts | Unique Part #s | Total Parts | Unique Part #s | Total Parts |  | 
Completed Projects | 77 | 382 | 49 | 168 | 159 | 859 | 100 | 1778 | 385 | 3187
Active Projects | 7 | 24 | 0 | 0 | 12 | 72 | 3 | 7 | 22 | 103
Total Projects | 84 | 406 | 49 | 168 | 171 | 931 | 103 | 1785 | 407 | 3290

## Slide 20
Notes: End Card – Put this slide at the end of presentations.